## Slide 1: FLOWSERVE NAF
Trunnball DL Product Presentation

## Slide 2
What is the NAF Trunnball DL?
High performance ball valve
Metal or soft seated
Full bore, two piece body
Trunnion mounted ball
Designed for both on-off and control applications

## Slide 3
NAF Trunnball DL design
Spring loaded stem seal packing > Minimized risk for non-planned plant downtime and emissions to atmosphere
Up to 250°C/482°F in it’s standard configuration > Reduced inventory need due to the temperature coverage
Blowout-proof stem providing a high torque transmission with a minimum mechanical backlash > Safe operation, better control performance

## Slide 4
NAF Trunnball DL design
Direct actuator mounting of the Turnex actuator which provides a high performance, vibration resistant, compact valve package > Lower maintenance cost, better control performance
Spring loaded metal seats with a rigid welded overlay of Alloy 6 or alternatively metal supported, reinforced PTFE seats > High tighness even at low differential pressures
Trunnion plates with large low friction bearings mounted inside the valve body> Minimized risk for external leakage and better control performance

## Slide 5
NAF Trunnball DL design
Unique Z-trim™ option that minimizes cavitation and noise and has an excellent control characteristic > Better working environment, lower maintenance cost for wear, better control performance

## Slide 6
NAF Duball DL design
Blow out proof stem
Metal- or soft seated
Trunnion mounted Ball,
Standard or Z-trim
Spring loaded Stem Packing
(V-rings)
Two-piece Off-centre
Direct mounting
of Turnex
Low friction bearings

## Slide 7
Spring loaded stem seal packing
R-PTFE V-rings >
  multistage seal,
  minimum risk for leakage
  250°C/482°F as standard
Wave spring, preload > no need for manual re-tightening
High thrust, anti-friction washer > can take high pressure and high cycle applications

## Slide 8
NAF Trunnball DL, standard seats

## Slide 9
NAF Trunnball DL, standard seats
Lip (part of the support ring) > Eliminates the risk of spring being drawn into flow
Metal support ring > Prevents the soft seat from plastic deformation under load
Metal seats with a rigid welded overlay of Alloy 6 (min 2 mm)
Ball
Ball
Seat
Seat
Body
Body
Lip (part of the seat) > Eliminates the risk of spring being drawn into flow
Both seat designs are very rugged and rigid > Minimized risk for non-planned plant downtime due to seat damage
Metal seat standard
Soft seat standard
Seal
Seal
Spring
Spring
Support ring

## Slide 10
Trunnball DL, some typical applications
Pulp stock handling in fiberline (washing, oxygen delignification, screening, bleaching) in a pulp plant
General ball valve applications with higher differential pressures
Pressure control of low- and medium-pressure steam
Control applications where a high Cv is needed
Gas pressure control (with Z-trim)
High flow slurry and erosive medium applications
NAF Trunnball in oxygen delignification

## Slide 11
NAF Trunnball DL
Material: CF8M, WCB (Duplex, Hastelloy, Titanium etc.)
Sizes: DN150-DN900
ANSI 6” – 36” Full bore
Pressure class: PN10-PN40
ANSI Class 150 & 300
Tightness class: PTFE-seats: EN 12266-1:2012, rate A (ISO 5208, rate A)
Metal seats: EN 60534-4, Class V
ANSI FCI 70-2, Class V
Connection: Flanges
Temperature: -30 - 250°C
-22 - 482°F

## Slide 12
NAF Duball DL + NAF Trunnball DL
The complete range of NAF flanged full port ball valves
NAF Duball DL, floating ball
NAF Trunnball DL, trunnion mounted ball
Maximum allowed dp

## Slide 13
Summary of features and benefits of
NAF Trunnball DL
State-of-the-art spring loaded stem seal packing that requires no maintenance and ensures safe operation in automated on-off and control service > Minimized risk for non-planned plant downtime and emissions to atmosphere
With the PTFE V-ring stem seal, the valve can take applications up to 250°C/482°F in it’s standard configuration > Minimized inventory need due to the temperature coverage
Direct actuator mounting capabilities of the Turnex actuator which provides a high performance, vibration resistant, compact valve package > Lower maintenance cost, better control performance
Sturdy, blowout-proof stem providing a high torque transmission with a minimum mechanical backlash > Safe operation, better control performance

## Slide 14
Unique Z-trim™ option that minimizes cavitation and noise and has an excellent control characteristic > Better working environment, lower maintenance cost for wear, better control performance
An extensive size range, DN25/1”” up to DN900/32” together with NAF Duball DL > Cover the majority of ball valve applications in a plant
Easy-to-service arrangement, due to the off-center joint face of the valve body, which allows for easy replacement of the ball and seals, without the need for removing the stem and actuator > Minimized time for maintenance and plant downtime
Spring loaded metal seats with a rigid welded overlay of Alloy 6 or alternatively metal supported, reinforced PTFE seats > High tightness even at low differential pressures
Summary of features and benefits of
NAF Trunnball DL

## Slide 15
. . and our other rotary control valves . .
NAF Torex
High performance, triple offset butterfly valve
DN80/3”-DN700/28”, wafer&lug style
PN10-PN40/ANSI Class 150 and 300
NAF Setball
High performance, V-port, segmented ball valve
Wafer, Flanged, SF and MC-pulp versions
DN25/1”-DN500/20”
PN10-PN40/ANSI Class 150 and 300
NAF Duball DL
High performance, floating ball valve.
DN25/1”-DN400/16”
PN10-PN40/ANSI Class 150 and 300

## Slide 16
Appendix 1: Maximum allowed
differential pressure for Trunnball DL

## Slide 17
Thank you for your attention